## Slide 1: (2022) Dynamic UPF placement and chaining reconfiguration in 5G network
Irian Leyva-Pupo, Cristina Cervelló-Pastor, Christos Anagnostopoulos, Dimitrios P. Pezaros
2022 Computer Networks (IF=4.4)

## Slide 2: Outline
Introduction
Optimal UPCR (ILP model & heuristic)
Dynamic UPCR (Reconfiguration mechanism)
Performance Evaluation

## Slide 3: Introduction
Research topic :
5G UPF (Chain) Placement
UPF-P Reconfiguration
Notes: Placement :
在 4G 時代是集中部屬，5G 則是引入 edge computing，要分散式部屬到距離使用者更近的位置，常見的就是放在 BS 附近，而非 DC，以滿足 5G URLLC 情境對低延遲通訊的需求
Edge 好處 : 降低延遲 ; 壞處 : 服務範圍小
Reconfig :
user mobility + edge deployment => session relocation
方法一 : UPF 位置固定不變 ; 方法二 : UPF 位置動態變化 (Reconfig.)
  需放圖
  方法一有會有固定(穩定範圍)
  方法二可以保持更少的 UPF，對使用者沒什麼影響 (反正延遲夠低就行)，Reconfig. 更多是對營運商好
Reconfig (readjust) may produce service interruption => find optimal time to Min. reconfig. Event as possible
綜上 :
目標 : 在滿足 5G 使用者需求(主要是低延遲)的情況下，盡量減少營運商的營運部屬成本

## Slide 4: 5G UPF Placement
4G central deployment of PGW → 5G edge deployment of UPF
Advantage :
Lower end-to-end latency
Less network congestion (higher scalability)
Disadvantage :
Smaller serving area per UPF (more frequent session relocation / reassignment)
Higher OPEX & CAPEX

## Slide 5: UPF-P Reconfiguration
Static UPF placement :
UPF

## Slide 6: UPF-P Reconfiguration
After some time :
UPF

## Slide 7: UPF-P Reconfiguration
Dynamic UPF placement (Reconfiguration) :
UPF

## Slide 8: Ch.1 - Introduction
Research topic :
5G UPF (Chain) Placement
UPF-P Reconfiguration
Main goal :
Cost reduction while ensuring 5G service requirements are fulfilled

## Slide 9: Ch.1 - Introduction
Main Contribution :
Formulated as ILP model, considered Service Function Chain (SFC) order and UPF-specific requirements
Design a heuristic algorithm
Applying Optimal Stopping Theory (OST) to find optimal scheduling reconfiguration

## Slide 10: Ch.3 – Optimal UPCR
UPCR : UPF Placement and Chaining Reconfiguration
Notes: 實際 system model 和這個示意圖是有差距的
沒分 macro / micro，總之就是 gNB (RAN) (BS)
沒有 aggregation point，只有 candidate location，所以比如右下的 agg. point 就會被省略掉
System model 是以 session 為單位考慮部屬，而不是 gNB-UPF 的配對
System model 考量的是 UPF chain (3 種)
System model 不只要部屬「點」，也要佈「線」
第三點之後是在後續才會說明

## Slide 11: Ch.3 – Optimal UPCR
UPF chain considered in this paper :
1.
2.
3.
Notes: UPF chain 有 3 種，並且(正好) UPF 也分 3 種 : A-UPF、I-UPF、BP

## Slide 12: Ch.3 – Optimal UPCR
UPF
Notes: 在剛才的舉例，可以以 BS 為單位考慮 UPF 部屬位置 (BS-UPF)

## Slide 13: Ch.3 – Optimal UPCR
UPCR : UPF Placement and Chaining Reconfiguration
I-UPF
UPF
BP
UPF
Notes: 承上，但如果是這裡的 UPF chain，就要以更細的 session 為單位考慮 UPF 部屬，因為即便出自同一個 BS 的 sessions 也可能需要走不同的路徑
System model 和這個示意圖是有差距的 :
System model 是以 session 為單位考慮部屬，而不是 gNB-UPF 的配對
System model 考量的是 UPF chain (3 種)
System model 不只要部屬「點」，也要佈「線」

## Slide 14: 補充 : Integer Linear Programming (ILP) Model
Example of Linear Programming (LP) – Furniture Problem
Chair = 5 woods + 10 hours, Price = $ 45
Table = 20 woods + 15 hours, Price = $ 80
We have 400 woods and 450 hours
Question : How to maximize revenue ?

## Slide 15: 補充 : Integer Linear Programming (ILP) Model
Example of Linear Programming (LP) – Furniture Problem
Chair = 5 woods + 10 hours, Price = $ 45
Table = 20 woods + 15 hours, Price = $ 80
We have 400 woods and 450 hours
Question : How to maximize revenue ?
Answer :
(Objective)
(Constraints)

## Slide 16: 補充 : Integer Linear Programming (ILP) Model
Objective : ⇒ is decision variables
Linear Programming : decision variable is real number
Integer (Linear) Programming : decision variable is integer
Mixed Integer (Linear) Programming : some of decision variables are integer, some of them are linear
Conclusion : IP (ILP) ⊂ MIP(MILP) ⊂ LP

## Slide 17: Ch.3 – Optimal UPCR
Objectives :
: Node activation cost
  e.g. Energy consumption of new activated server
: vNF Deployment cost
: vNF running cost
: vNF migration cost
: Routing cost
  e.g. Delay/distance between gNB-UPF
: Session reassignment cost

## Slide 18: Ch.3 – Optimal UPCR
Objectives :
: Node activation cost
  : cost component
  : 1 if candidate node is activated
: Routing cost
  : propagation delay for path

## Slide 19: Ch.3 – Optimal UPCR
Constraints :
Infrastructure resource constraints
vNF placement constraints
vNF assignment constraints
Path mapping constraints
UPF constraints (location constraints)
Reconfiguration constraints

## Slide 20: Ch.3 – Optimal UPCR
Constraints :
Infrastructure resource constraints
  (8) : 確保 server 有足夠計算資源服務其上 vNFs
  (9) : 確保 vNF 有足夠計算資源服務其上 sessions
  (10) : 確保所選的 physical path 有足夠通訊頻寬服務其上 sessions

## Slide 21: Ch.3 – Optimal UPCR
Constraints :
vNF placement constraints
  (11) : 確保沒有運行 vNF 的 server 是關閉的
  (12) : 確保 vNF 開在有支援此 vNF 的 server 上
  (13) : 確保 vNF 只被部屬於一個 server 上
  (14) : 限制每種類 vNF 的部屬數量不超過規定上限

## Slide 22: Ch.3 – Optimal UPCR
Constraints :
vNF assignment constraints
  (15) : 如果 vNF 已部屬且類型正確，我們才能把 session 分配給該 vNF 服務
  (16) : 確保運行中的 vNF 都有在為 sessions 服務
  (17) : 確保 session 的每個環節都只有一個 vNF 提供服務
  (18)(19) : 確保如果 SFCR 被分配到某個節點，那是因為該節點上已開啟相應的 vNF

## Slide 23: Ch.3 – Optimal UPCR
Constraints :
Path mapping constraints
  (20) : 如果有一條 logical link f → g，則 f, g 的部屬位置之間必須存在一條 physical path
  (21) : 確保 vNF f → g 之間至多只有一條 physical path，以避免迴圈形成
  (22) : 如果於 server n, m 間有一條 physical path，代表 n,m 上一定有運行 vNF f, g

## Slide 24: Ch.3 – Optimal UPCR
Constraints :
Path mapping constraints
  (20) : 如果有一條 logical link f → g，則 f, g 的部屬位置之間必須存在一條 physical path
  (21) : 確保 vNF f → g 之間至多只有一條 physical path，以避免迴圈形成
  (22) : 如果於 server n, m 間有一條 physical path，代表 n,m 上一定有運行 vNF f, g

## Slide 25: Ch.3 – Optimal UPCR
Constraints :
UPF constraints (location constraints)
  (24) : 確保服務一 session 的同類型 (type) vNFs 部屬於不同 servers，e.g. 兩個 A-UPF 不在同一位置
  (25) 確保服務一 session 的 I-UPF 和 A-UPF，雖然不同類型，但也部屬於不同 servers

## Slide 26: Ch.3 – Optimal UPCR
Constraints :
Reconfiguration constraints
  (26) : 確保 migration indicator 數值正確
  (27) : 確保 deployment indicator 數值正確
  (29) : 確保 session reassignment indicator 數值正確

## Slide 27: Ch.3 – Optimal UPCR
Constraints :
QoS constraints :
  (30) : 確保沒有 latency violations

## Slide 28: Ch.4 - Dynamic UPCR
Because of user mobility, system need to reconfigure (readjust) UPF placement to better serve users
Reconfiguration bring extra cost ⇒ Min. reconfig. event
Decide reconfigure or not based on Optimal Stopping Theory (OST)

## Slide 29: Example of OST – Hiring Problem
candidates apply for 1 job
Decide to hiring him or not on the spot
Objective : find the best candidate
Hired

## Slide 30: Example of OST – Hiring Problem
Hire the first candidate ⇒ 1/n chance to be the best
If median score is known, hire the first who surpass median ⇒ 1/2 chance to be the best
Problem is we don’t know median

## Slide 31: Example of OST – Hiring Problem
Strategy : sampling (rejecting) the first candidates, hire the first one better than sample average
Problem : how to select the best sample size ?
Answer : sample size = n/e = n/2.71 ⇒ 37% to be the best
Notes: 簡單來說 OST 針對的是一個 markov decision problem (random process problem)，每個 state 你都有固定兩個選擇 : continue or stop
而 OST 的策略就是 : 觀察(起手 continue) -> 做出更聰明的決定

## Slide 32: Ch.4 - Dynamic UPCR
Back to UPCR problem :
Define latency violation as session latency > requirement
Number of latency violations at time is
Assume system can tolerate a certain number of latency violation, defined as threshold
Notes: 一開始部屬是 0但隨著用戶移動，會開始產生 Lt

## Slide 33: Ch.4 - Dynamic UPCR
Applying OST to UPCR problem :
Decide whether to reconfiguration based on
Reconfiguration bring extra cost ⇒ Aim to min. reconfiguration event ⇒ Reconfig. when as close to as possible without exceeding it
Notes: 一開始部屬是 0但隨著用戶移動，會開始產生 Lt

## Slide 34: Ch.4 - Dynamic UPCR
Reconfiguration cost function :
: cost coefficient
: expected number of relocated session
: number of latency violations
: weight factor
: expected reconfiguration cost
Notes: Session relocation 發生於當服務 session 的任一 UPF 發生位移

## Slide 35: Ch.4 - Dynamic UPCR
Reconfiguration cost function :
Notes: 為何我認為會是如此 ?

## Slide 36: Ch.4 - Dynamic UPCR
For each time epoch , we must take one of the following actions :
Stop observing , and reconfigure the system
Continue to next time epoch
Objective : Finding optimal time epoch , which min. reconfiguration cost
Notes: OST : choosing a time to take action based on sequential observed random variable X0~Xt to minimize an expected cost

## Slide 37: Ch.4 - Dynamic UPCR
Using 1-Step Look Ahead (1-SLA) rule to describe stopping time :
1-SLA rule is an myopic(短視近利) approach
1-SLA rule will top whenever stopping now is better than stopping in next step

## Slide 38: Ch.4 - Dynamic UPCR
Theorem 1 :
In monotone stopping rule problems, the 1-SLA rule is optimal
Proof :
skipped in paper

## Slide 39: Ch.4 - Dynamic UPCR
Theorem 3 :
The 1-SLA rule is optimal and minimizes the expected cost (this problem is monotone)
Proof :
is non-increasing regarding to , if
Notes: 所以 1-SLA 什麼時候會 call for stop? 其實就是預測 Lt+1 >θ 的時候， 所以重點就是如何預測 Lt+1

## Slide 40: Ch.4 - Dynamic UPCR
Theorem 3 :
The 1-SLA rule is optimal and minimizes the expected cost (this problem is monotone)
Proof :
is non-increasing regarding to , if
But is not non-decreasing regarding to
Notes: 所以 1-SLA 什麼時候會 call for stop? 其實就是預測 Lt+1 >θ 的時候， 所以重點就是如何預測 Lt+1

## Slide 41: Ch.4 - Dynamic UPCR
Theorem 2 :
Given and , then can be translated as :
⇒

## Slide 42: Ch.4 - Dynamic UPCR
Theorem 2 proof :
Notes: 沒有解釋如何預測 Lt+1，雖然我猜射應該是由 L0~t 去預測，但具體怎麼算出機率就不知道了

## Slide 43: Ch.3 – Optimal UPCR
Heuristic algorithm - Dynamic priority and cautious UPCR
The algorithm has 4 phases :
Select sessions to be remapped
Find possible candidate locations
Map sessions
Improve solutions by random relaxation
Notes: ILP model : 太慢 => heuristic

## Slide 44: Ch.3 – Optimal UPCR
Phase.1 Select sessions to be remapped
How many sessions should be reconfigured ?
Besides latency violated sessions, additional percentage of sessions with lowest QoS will be release and remapped

## Slide 45: Ch.3 – Optimal UPCR
Phase.2 Find possible candidate locations
Line 9 : Find available candidate servers
Line 11 : Find possible candidate servers
Line 12 : Classify critical session, if servers vNFs

## Slide 46: Ch.3 – Optimal UPCR
Phase.3 Map sessions
Line 13 : Sort sessions by various criteria, mapping the most demanding or the most critical sessions first.
Line 16 : sessions remapping function

## Slide 47: Ch.3 – Optimal UPCR
Phase.3 Map sessions
Line 21 : if server run out of resources, update candidate servers list and re-sort sessions priority

## Slide 48: Ch.3 – Optimal UPCR
Phase.4 Improve solution by random relax

## Slide 49: Ch.3 – Optimal UPCR
Phase.4 Improve solution by random relaxation
Randomly select a vNF and unmap its sessions
Repeat phase 2-3 to remap these sessions to other vNFs ( servers )
Check if the overall reconfig. cost been reduced
Iterate times of step 1-3
Determine cause of vNFs (new deployment or migration)

## Slide 50: Ch.5 – Performance Evaluation

## Slide 51: Ch.5 – Performance Evaluation
Heuristic alogorithm :
Partial unmapping
Improvement stage
Performance
Reconfiguration mechanism :
Number of reconfiguration events
Number of latency violations

## Slide 52: 1. Partial Unmapping
When reconfig. triggered, how many session should we remap ?
Light blue : without reconfig. cost Dark blue : with reconfig. cost
Notes: 在不考慮 reconfig. Cost 情況下，session remap 愈多愈能找到更好部屬 (左淺藍)，但如果考慮到 reconfig. Cost ，則不是 session remap 愈多愈好

## Slide 53: 2. Improvement stage

## Slide 54: 3. Heuristic Algorithm Performance
Compare with (sorted) greedy approach
When placing vNF, do not consider the next vNF that form the SFC

## Slide 55: 3. Heuristic Algorithm Performance
Compare with ILP model

## Slide 56: Reconfiguration Mechanism
Compare Optimal Scheduling Reconfiguration (OSR) with :
Periodic Scheduling Reconfiguration (PSR)
Skeptical Scheduling Reconfiguration (SSR)
  Authors’ previous work
  Main difference is reconfiguration cost function
  Previous :
  Current :
  Current work

## Slide 57: 1. Reconfiguration event

## Slide 58: 2. Number of latency violation

## Slide 59: Q & A